## Slide 1: Preliminary L3 Safety Concept
ESS3
Detail need further safety analysis. Draft only for discussion

## Slide 2
Agenda Overview
L3 system scope assumption
L3 safety concept
Detail need further safety analysis. Draft only for discussion

## Slide 3: L3 system scope assumption(refer to ECE R157e)
L3 Feature and Architecture Alignment
      Driver eye-off、Driver monitor、10s hand-over to driver
      Speed(0-60 kph)
      Environment condition
            Road profile (curvature, elevation)
            No pedestrian
            physical separation
            night and day
          Lane keeping、Vehicle following、Target vehicle cut-in
      Safe stop in lane(MRM)
More scenario extended, more challenge to system performance  more FuSa & SOTIF challenge
Detail need further safety analysis. Draft only for discussion
Preliminary L3 safety concept

## Slide 4: Proposal Emergency Operation & Safe State
Proposal
(cost saving)
Safe States
  Option 1: Deactivate until repair/ MRM finished
  Option 2: Provide functionality without time restrictions within restricted vehicle operating states (ASIL capability ≥ ASIL (hazard))
Preliminary L3 safety concept
FTTI
Teotti
Safe State:
Functionality
deactivated
Fault
*Source: ISO 26262-10:2018
Fail operational
Fail active (functionality)1
Fail degraded (functionality)1
Fail operational (functionality)1
Replace with
Distinguish between
1 A given element can be fail passive for one functionality and fail active for another
Provide functionality with reduced performance
Provide functionality with nominal performance
Detail need further safety analysis. Draft only for discussion

## Slide 5: Preliminary top level safety concept
Preliminary L3 safety concept
Urban/Expressway- ASIL D(S3 C3 E4)
Highway- ASIL B(S1 C3 E4)
Max_Vspeed 60kph
Urban/Expressway/Highway- ASIL C(S2 C3 E4) to car
ASIL D(S3 C3 E4) to pedestrian
Keep ODD within 60kph- ASIL D(S3 C3 E4)
Max_Vspeed 60kph
UI loss of deceleration  ASIL D
UI loss of lateral control
 Highway(ASIL B), urban/expressway(ASIL D)
Fail-degraded related
Detail need further safety analysis. Draft only for discussion

## Slide 6: Preliminary safety concept allocation
Preliminary L3 safety concept
Detail need further safety analysis. Draft only for discussion

## Slide 7: Preliminary safety concept allocation
Preliminary L3 safety concept
Detail need further safety analysis. Draft only for discussion

## Slide 8: Preliminary POC safety minimum requirements
Preliminary L3 safety concept
 | WP no breakdown yet | POC minimum scope | Comments
1 | Top down safety concept derivation incl. concept level and system level incl. global core team review | Part | Potential risk: No maturity safety concept and safety development experience; No maturity SOTIF development experience; Compliance risk and release SW to COEM w/o safety implementation; Others?
2 | (ASIL xx) HW+ safety development(DFA/SSA/FFI/FMEDA/safety arch etc.) incl. global core team review | Part | 
3 | (ASIL xx) ASW safety development (DFA/SSA/FFI/FMEDA/safety arch etc.) | Part | 
4 | (ASIL xx) V&V | Part | 
5 | (ASIL xx) supporting process | Part | 
6 | (ASIL xx) safety management | Part | 
7 | SOTIF(management/supporting/engineer, analysis,concept,strategy,area2/3 test etc.) | Part | 
8 | ICV regulation support such as documentation, simulation, test(FIU) etc. | All | 
Detail need further safety analysis. Draft only for discussion