## Slide 1: HAD Basic Training FCT – Function Development Markus Mayer-Spohn

## Slide 2: Agenda
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
2
Function development
  Overview
  Typical Functions
FCT Architecture
  State Machine
  Arbitration
  HMI
Case example HWA
Questions

## Slide 3: Development Overview
HAD Basic Training
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
3
XIL
Testinfrastructure (Vehicle Build Up)
Testinfrastructure (Simulation)
Functional Safety, Validation
Connectivity
System Integration
VMCCore
DACore
Planning
Environment Sensing (ENS-x)
Perception (PER)
Situation Analysis (SIT)
Function Behavior (FCT)
Reaction Pattern Manager (RPM)
Vehicle Motion & Control (VMC)
Maps & Localization (MAP/LOC)
Major Functional Building Blocks & Data Flow
Major Topics beyond Function Development

## Slide 4
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
4
Function development in general

## Slide 5: Overview
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
5
Function ownership for comfort and safety functions based on multisensory systems
  Definition and development of the corresponding interface between DACore and functions (API)
  Definition and development of function part (FCT)
  Customer interface
  Coordination of sub-systems being involved in function realization
  Review of solutions within the customer projects in order to assess their suitability for re-use within the platform
Function Ownership from sensor to the actuator

## Slide 6: Comfort Functions
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
6
HWA – Highway Assist Plus
  Partially automated vehicle control on highways and well structured country roads including automated lane change (level 2)
  Speed range: 0…180 km/h
  Automated lane change by driver confirmation (triggered by indicator) Speed range: 60…130 km/h
  Optional: Safe stop in ego lane (level 2 safe stop)
  Automated transition to HWA Basic while no automated lane change is requested
TJA – Traffic Jam Assist / HWA basic
  Partially automated vehicle control at all speed ranges on highways and well structured country roads (level 2)
  Speed range: 0…60 km/h (TJA) 0…180 km/h (HWA basic)
  Hands-off driving: unlimited up to 10 km/h, speed-dependent time-limit otherwise
  Driver takeover: lane change necessity, irregular obstacles in lane, lane not drivable (width, curvature, …)
Notes: Level 2 Safe Stop in ego lane – JLR name: DCR (Driver Condition Response)

## Slide 7: Safety Functions
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
7
LSS – Lane Support Systems
  Lane Keeping (comfort) – Detection of unintentional leaving of the ego lane
    Visual and/or audible warning combined with haptical warning (LDW) or lateral countersteering (LKA) – Speed range: 64…180 km/h
  Lane Keeping (emergency) – Detection of leaving the ego lane in case there is a potential threat such as a road boundary or oncoming vehicle (ELK)
    Lateral countersteering to keep the vehicle in the ego lane and avoid a threat.
  Evasive Steering Support (ESS)
    Lateral guidance of the vehicle during a critical evasive maneuver (driver initiated)
AEB – Automated Emergency Brake
  AEB Family
    City-Urban AEB (CuAEB)
    Pedestrian AEB (PAEB)
    Cyclist AEB (CAEB)
    Front Cross Traffic Alert (FCTA)
    Left Turn Assist (LTA)
    High Speed AEB (speed range up to 160 km/h)

## Slide 8
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
8
Sub-system FCT (Function)

## Slide 9: Architecture Overview
DACore
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
9
FCT
RPM
SIT
PER
VMCore
Notes: Platform DACore as basis for function development
Contains main sub-systems PER, SIT and RPM
Other services included as well: Diagnostics, Network, Degradation, …
Function layer on top of DACore using API to realize the functions

## Slide 10: Detailed FCT Architecture
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
10
FCT
Function State Machines
Function Arbitration
RPM
SIT
HMI Controller
Notes: Function Layer consists of 3 main blocks
Function State Machines
  Realizing function behaviour
  Containing individual function state machines
Function Arbitration
  Defining interaction between the functions
Human Interface Controller
  Realizing the output interface to the driver
  Optical, acoustic or haptic signals

## Slide 11: Detail – Function State Machine
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
11
State Machine Scope
Behaviour Manager
Generic platform framework with reference implementation
State Machine
FIP
Function Input Processing
SPP
Signal Pre-Processing
PPBI
Preparation of internal signals and calculation of generic conditions for all state machines.
Function state machine
Activation trigger
Prevention/Switch Off
Generation of “behaviour specifications” for SIT depending on function states
Preparation, preprocessing and mapping of external signals (CAN, HMI, …) to internal signals
Vehicle Specific
FCT
Function State Machines
Function Arbitration
HMI Controller
Notes: Detailed view on the function state machine part
SPP – Signal Pre-Processing
Formerly known as PPBI sub-system in SystemB+
Mapping of network signals to internal signals
  HMI Input signals e.g. ACC buttons, indicator switch
  Function relevant vehicle information e.g. Door Status
  Customer Specific signals for functions
  Remark: other vehicle signals, e.g. vehicle speed or yaw rate, are integrated in the PER SPP and provided internally via DADDY ports
This mapping is highly vehicle specific
SPP is running in 10ms cycle to recognize all network signals and e.g. short button press signals
FIP – Function Input Processing
Generic usage of the SPP inputs signals and the input signals of other Sub-Modules
These generic signals could be used by all function state machines  benefit: signal has to be integrated only once in the system
Generic conditions could be calculated out of the SPP input signals, e.g. Driver precondition (Doors, Seatbelt closed)
State Machine
Individual state machines could be implemented for each function
Usage of FIP signals and conditions as input triggers
State Machine specific conditions
  Activation Trigger
  Activation Prevention Condition
  Switch Off Conditions
State Machine Handling
Behaviour Manager
Generation of behaviour specifications for SIT depending on the function state
  Only relevant calculation requests are sent to DACore in order to spare calculation resources
  Multiple scenarios will be requested in parallel to be predicted by DACore
    E.g. AEB in parallel to a Lane Driving for ACC
  Later FCT will decide which one is relevant to be executed
Starting point for DACore behaviour generation: SIT API interface to trigger the DACore calculations
If no behaviour is specified, the DACore will not provide any scenario to realize a function

## Slide 12: Architecture Overview – State Machines
FCT
Function State Machines
Function Arbitration
HMI Controller
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
12
RPM
SIT
LSS
…
ACC
AEB
HMI Requests
Vehicle Conditions
Behaviour Specification
Behaviour Manager
States
Evaluated Behaviour
Notes: Details in FCT Architecture - State Machine
HMI Requests
  Input button signals
  Vehicle configuration via multimedia display
Vehicle conditions
  Ego velocity
  Yaw rate
  Door Status …
Individual State machines for the functions
  Providing function status (Inactive, Active, Ready, Failure, …)
Behaviour Manager
  Generating behaviour specification as input to SIT
Summarize already known DACore Procedure which is following in DACore
SIT running behaviour strategy evaluation
Prediction being done be RPM for each specified behaviour
SIT evaluating all of these behaviors and generating metrics to describe feasibility of these behaviors
  Evaluated behaviours being provided to function arbitration block

## Slide 13: Detail – Function Arbitration
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
FCT
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
13
FCT
Function State Machines
Function Arbitration
HMI Controller
Selected Behaviour
Filtering based on SM state and metric evaluation
Arbitration Matrix
Evaluated Behaviours
Function State Machines
SIT
Filtering based on state machine status
Filtering based on metric evaluation
(Necessity, CollisionProbability …)
Prioritization between remaining functions
Function States
RPM
Notes: Input to the arbitration block
Function states from function state machines
  Which features is currently active, e.g. depending on driver input via buttons
  Maybe in the meantime some precondition is not fulfilled any more, so here we can react on the latest state machine input (being evaluated more frequently (20ms) than the DACore calculations (~100ms)
Evaluated behaviours from SIT
  Each requested behaviour is evaluated by SIT
  Evaluated behaviours contain metrics which show if a behaviour is feasible and could be executed
First block is Filtering based on state machine
  Only if the state machine is still active, take this behaviour into account
Second block is filtering based on metrics evaluation
The metrics of each behaviour are evaluated
  E.g. lane driving for ACC only done if collision probability is very low
  Or necessity of an AEB or lateral control system has to be high in order to choose this behaviour
Now the number of behaviours to be executed should be reduced already.
Final block is the arbitration matrix to decide based on priority
Only one behaviour is allowed to be executed by RPM using lateral and/or longitudinal control (warning or HMI only behaviours could run in parallel)
E.g. AEB has a higher priority than an ACC

## Slide 14: Architecture Overview – Arbitration
FCT
Function State Machines
Function Arbitration
HMI Controller
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
14
RPM
SIT
LSS
…
ACC
AEB
HMI Requests
Vehicle Conditions
Behaviour Specification
Behaviour Manager
States
Evaluated Behaviour
Filtering
Arbitration
Filtered Behaviour
Selected Behaviour
Notes: Details in FCT Architecture – Arbitration
Signal Flow
Evaluated behaviour from STI to Arbitration Block
Filtering to reduce the amount of evaluated behaviors
Arbitration to select one behaviour to be executed by RPM
-> next block HMI

## Slide 15: Detail – Human Machine Interface
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
15
FCT
Function State Machines
Function Arbitration
HMI Controller
HMI Controller
Function States +
HMI Info
Arbitration Result
Introspection Data
RPM
SIT
HMI Signals
Cluster
Head-up
Audio
Multimedia
  HMI Controller Input
  Function states from feature state machines and HMI specific feature data
  Arbitration result in order to decide which feature is currently being executed
  Introspection Data from the sub-systems RPM and SIT
    Data represents the internal state of the DACore sub-systems
    RPM:
      E.g. currently executed reaction pattern and specific data like target object availability or set-speed
    SIT:
      E.g. lane availability status
  HMI Controller Output
  HMI output signals are highly depending on the customer vehicle configuration

## Slide 16: Architecture Overview – HMI
FCT
Function State Machines
Function Arbitration
HMI Controller
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
16
RPM
SIT
LSS
…
ACC
AEB
HMI Requests
Vehicle Conditions
Behaviour Specification
Behaviour Manager
States
Evaluated Behaviour
Filtering
Arbitration
Filtered Behaviour
Selected Behaviour
Arbitration Result
Optic & Acoustic Output
Function Info
HMI State Machine Logic
Notes: Details in FCT Architecture – Complete Overview

## Slide 17
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
17
Case example:
Highway assist with
automated lane change
Notes: Next Step is Use Case example to demonstrate the signal flow and the usage of the FCT architecture blocks

## Slide 18: Scenario description – Automated Lane Change
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
18
Automated lane driving
- Longitudinal and lateral control in ego lane
Step 1
Lane change trigger
- Feasibility calculation
- Longitudinal and lateral control in ego lane
Step 2
Automated lane change
- Longitudinal and lateral control in new target lane
Step 3
Automated lane driving
- Longitudinal and lateral control in new ego lane
Step 4

## Slide 19: Detailed Signal Flow – Step 1
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
19
FCT
Function State Machines
Function Arbitration
RPM
SIT
HWA
AEB
HMI Requests
Vehicle Conditions
Behaviour Specification
Behaviour Manager
States
Evaluated Behaviour
Function States
HMI Controller
Automated lane driving
- Longitudinal and lateral control in ego lane
Step 1
Ego Speed
Yaw Rate
Set Speed = 125
Time Gap = 2
Set + pressed
Lane Driving
Set Speed = 125
Time Gap = 2
HWA active
AEB available
Emergency Brake
Set Speed = 120
Time Gap = 2
Lane Driving
CollisionProb = 0
Emergency Brake
Necessity = 0
Function State Machine
Set Speed = 120
Time Gap = 2
HWA active
AEB available
Check conditions
Speed within limits
Yaw rate below threshold
Check conditions
Speed within limits (60 to 130 kph)
Button inputs (set speed, time gap, indicator)
HWA
AEB
Notes: Initial:
Lane Driving with
Set Speed = 120
Time Gap = 2
Next step is button press “Set +”  increase set speed by 5 kph
Lane Driving with
Set Speed = 125
Time Gap = 2
Behavior Manager:
Create two behaviors:
lane driving with parameters set speed and time gap
Emergency Brake
Send to SIT and perform prediction by RPM and send back to SIT
Evaluation is done by SIT and each behaviour gets some describing metrics.
Send back to FCT
Next-Slide  Arbitration

## Slide 20: Detailed Signal Flow – Step 1
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
20
FCT
Function State Machines
Function Arbitration
RPM
SIT
HWA
AEB
HMI Requests
Vehicle Conditions
Behaviour Specification
Behaviour Manager
Evaluated Behaviour
Function States
HMI Controller
Automated lane driving
- Longitudinal and lateral control in ego lane
Step 1
Filtering
Arbitration
Filtered Behaviour
Selected Behaviour
Arbitration Result
Function Info
HWA lane driving
Set speed = 125
Time gap = 2
Optic & Acoustic Output
States
Function Arbitration
Filtering
Arbitration
Filtered
Behaviours
Check function state
Evaluate SIT metrics
Prioritization
HWA active
AEB available
Lane Driving
CollisionProb = 0
Emergency Brake
Necessity = 0
Notes: Arbitration
Filtering
If the preconditions for feature activation are no longer valid, remove the evaluated behaviour
  E.g. the driver deactivated the feature, or the speed range is no longer in the valid range
Check if the SIT metrics are in a valid range
  Collision probability low
  Necessity high
In our case
  Lane Driving OK
  AEB not ok due to low necessity  filter out
Arbitration
Prioritization between the multiple behaviours if required
Lane Driving is chosen and sent to RPM for execution (longitudinal and lateral control)
In parallel, HMI output signals are generated

## Slide 21: Detailed Signal Flow – Step 2
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
21
FCT
Function State Machines
Function Arbitration
RPM
SIT
HWA
AEB
HMI Requests
Vehicle Conditions
Behaviour Specification
Behaviour Manager
States
Arbitration
Function States
Evaluated Behaviour
HMI Controller
Lane change trigger
- Feasibility calculation
- Longitudinal and lateral control in ego lane
Step 2
Set Speed = 125
Time Gap = 2
Indicator left
Lane Change Left
Set Speed = 125
Time Gap = 2
HWA left
AEB available
Emergency Brake
HWA active
Filtering
Filtered Behaviour
Selected Behaviour
Lane Change
CollisionProb = 0
Emergency Brake
Necessity = 0
HWA lane change left
Set speed = 125
Time gap = 2
Optic & Acoustic Output
Arbitration Result
Function Info
Notes: Step 2:
Lane Driving with
Set Speed = 125
Time Gap = 2
Next step left indicator being set by the driver
State Machine will check activation condition and change to “HWA left” state
Set Speed = 125
Time Gap = 2
Now the same cycle as shown before is done
Behavior Manager:
Create two behaviors:
lane change left with parameters set speed and time gap
Emergency Brake
Send to SIT and perform prediction by RPM and send back to SIT
Now a feasibility is calculated if the lane change is possible  represented in collision probability
Evaluation is done by SIT and each behaviour gets some describing metrics.
Send back to FCT
Arbitration is done in the same way

## Slide 22: Detailed Signal Flow – Step 3
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
22
FCT
Function State Machines
Function Arbitration
RPM
SIT
HWA
AEB
HMI Requests
Vehicle Conditions
Behaviour Specification
Behaviour Manager
States
Arbitration
Function States
Evaluated Behaviour
HMI Controller
Automated lane change
- Longitudinal and lateral control in new target lane
Step 3
Set Speed = 125
Time Gap = 2
Lane Change Left
Set Speed = 125
Time Gap = 2
HWA left
AEB available
Emergency Brake
Filtering
Filtered Behaviour
Selected Behaviour
Lane Change
CollisionProb = 0
Emergency Brake
Necessity = 0
HWA lane change left
Set speed = 125
Time gap = 2
Optic & Acoustic Output
Arbitration Result
Function Info
Notes: Step 3:
Continue Lane Change with
Set Speed = 125
Time Gap = 2
Exactly the same procedure is now following again during the lane change.
Within the DACore SIT and RPM a new prediction and evaluation of the situation is done during the lane change.
If the situation is not getting critical (object in front or approaching vehicle from the rear), FCT will still get a low collision probability for the lane change and choose it again.
 RPM will continue with the lane change execution

## Slide 23: Detailed Signal Flow – Step 4
Function Development
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
23
FCT
Function State Machines
Function Arbitration
RPM
SIT
HWA
AEB
HMI Requests
Vehicle Conditions
Behaviour Specification
Behaviour Manager
States
Arbitration
Function States
Evaluated Behaviour
HMI Controller
Automated lane driving
- Longitudinal and lateral control in new ego lane
Step 4
Set Speed = 125
Time Gap = 2
Lane Driving
Set Speed = 125
Time Gap = 2
HWA left
AEB available
Emergency Brake
Filtering
Filtered Behaviour
Selected Behaviour
Lane Driving
CollisionProb = 0
Emergency Brake
Necessity = 0
HWA active
Lane Change completed
Arbitration Result
Function Info
HWA lane driving
Set speed = 125
Time gap = 2
Optic & Acoustic Output
Notes: Step 4:
Lane change is completed information provided by DACore  FCT continue with lane driving as before
Request Lane Driving with
Set Speed = 125
Time Gap = 2
Same cycle as in step 1 is done.

## Slide 24
Internal | Chassis Systems Control | CC-AD/EYF2 | 2017-11-17
© Robert Bosch GmbH 2017. All rights reserved, also regarding any disposal, exploitation, reproduction, editing, distribution, as well as in the event of applications for industrial property rights.
24
Questions?